## Slide 1: EWH Project: Liquid Medication Delivery System
Team Members:
Allison McArton
Angwei Law
Jonathan Meyer
Grant Smith
Padraic Casserly
Advisor: Dr. John G. Webster, Ph.D.
Client: Engineering World Health

## Slide 2: Background
2.1 million children are affected by HIV
Boehring Ingelheim developed anti-transmission drug: nevirapine
Packets of the drug are given to expectant HIV+ mothers
Pharmacies need a way to accurately dispense the medication into packets

## Slide 3: Problem Statement
Liquid medication bottle-top dispenser
Sterilely deliver fixed doses of liquid nevirapine into foil packages

## Slide 4: Design Specifications
Dispense 0.6mL (± 0.05mL) of medicine
Accurately deliver 400 doses; operable for 6 months
Seal medicine bottle and prevent contamination
Cost less than $2.00

## Slide 5: Previous Work
Based on fluid resistance
Requires precise manufacturing
Not tested with viscous fluid
(Feest, Maharaj, Mogen, Cira, 2008)

## Slide 6: Design 1: Horizontal Syringe
Pros
Cons
Must flip upside down to use
Requires manufacturing
Viscous liquid may reduce accuracy
Simple to sterilize

## Slide 7: Design 2: The Straw Design
Pros
Cons
Multi-step process
Requires manufacturing
Sterility concerns
Accurate and reliable
Minimal viscosity concerns

## Slide 8: Design 3: Two One-way Valves
Pros
Cons
Simple to manufacture
Independent of viscosity
Can be simplified for local manufacture
Valves may be expensive

## Slide 9: Valve Options
Ball Valve
Single Flapper Valve
Double Flapper Valve
Pros
Least variable
Readily Available
Cons
Pros
Variable
Cons
Easily made
Pros
Most variable
Cons

## Slide 10: Design Matrix
Design | Cost (out of 35) | Accuracy (out of 25) | Reliability (out of 25) | Ease of Use (out of 15) | Total (out of 100)
Horizontal Syringe | 17 | 20 | 20 | 5 | 62
Straw Design | 25 | 25 | 23 | 10 | 83
Two One-Way Valves | 25 | 25 | 25 | 15 | 90

## Slide 11: Future Work
Purchase materials and construct prototype
Procure or synthesize appropriate medication analog
Test device for accuracy and reliability
Evaluate valves
Make necessary modifications
Submit to EWH

## Slide 12: Questions?

## Slide 13: Acknowledgements
Dr. Webster
Engineering World Health
  Justin Cooper
  Dr. Malkin
Previous Design Team

## Slide 14: References
Engineering World Health (2009). “Engineering World Health: Senior Design Projects That Matter. ” Engineering World Health. Accessed Oct. 15, 2009, at <http://216.92.64.45/uploads/docs//09-10_EWH_Projects_that_Matter.pdf>
Feest, A., Maharaj, V., Mogen, B., Cira, N. 2008. “Final Report.” Accessed Nov. 19, 2009, at <http://homepages.cae.wisc.edu/~bme300/ewh_f08/secure/reports/ Final_Paper.pdf>